## Slide 1: Lecture 23: The Mathematics of Thermodynamics
Thermodynamic Potentials & Legendre Transforms CBE 20260 / Thermodynamics I

## Slide 2: Introduction: From Concepts to Math

## Slide 3: Moving from Concepts to Mathematics
So far: We analyzed equipment (turbines, pumps) and cycles using the 1st and 2nd Laws.
The Method: We relied heavily on tables and charts to find , , and .
The Problem: Where do those tables come from?
  You cannot directly measure Internal Energy () or Entropy () with a meter.
  You can only measure Temperature (), Pressure (), Volume (), and Heat Capacity ().
The Goal: Develop a mathematical framework to rewrite thermodynamics entirely in terms of measurable variables.

## Slide 4: The Fundamental Equation

## Slide 5: The Fundamental Equation of Thermodynamics
Let’s combine the First and Second Laws for a closed, single-component system.
First Law (Energy Balance):
Reversible Process Assumptions: * 2nd Law:
  Mechanical Work:
Substitute:

## Slide 6: Properties of the Fundamental Equation
Crucial Note: Even though we assumed a reversible process, , , and are all state functions.
This equation holds true for any process between two equilibrium states, reversible or irreversible!
It shows the “natural” independent variables for Internal Energy:

## Slide 7: Math Review: Exact Differentials

## Slide 8: Exact Differentials
Because , , and are state functions, their differentials are exact.
From multivariable calculus, for a function :
Let’s define the partial derivatives as coefficients:
Key Property: The mixed second partial derivatives must be equal:

## Slide 9: Applying Exact Differentials to U
Apply this framework to our fundamental equation:
We immediately see that:
Temperature and Pressure are simply the partial derivatives (or slopes) of the Internal Energy surface!

## Slide 10: Legendre Transforms

## Slide 11: The Variable Problem
contains all fundamental thermodynamic information.
However: and are highly inconvenient variables for chemical engineers. It is very hard to hold entropy constant in a lab.
We prefer to work with Temperature and Pressure.
We need to swap variables ( and ) without losing information.

## Slide 12: Why Simple Swapping Fails
Suppose we have a generic function and want to replace with the slope .
If we just write , it fails.
Parallel curves have the exact same slope at a given .
Swapping variables loses the integration constant—we lose physical data!

## Slide 13: The Legendre Solution
How do we uniquely identify a curve using only its slopes? Define it as an envelope of tangent lines.
Tangent line:
Solve for the y-intercept:
Because every point has a unique tangent intercept, the function contains the exact same info as !
The Legendre Transform:

## Slide 14: 1. Enthalpy ()
Let’s swap Volume () for Pressure (). The conjugate slope to is .
Definition:
Differential:
Substitute :
Result:
Natural variables: .

## Slide 15: 2. Helmholtz Free Energy ()
Let’s swap Entropy () for Temperature (). The conjugate slope to is .
Definition:
Differential:
Substitute :
Result:
Natural variables: .

## Slide 16: 3. Gibbs Free Energy ()
Let’s swap both , and . Apply the transform twice.
Definition:
Differential:
Substitute :
Result:
Natural variables: . (Most useful for Chemical Engineers!)

## Slide 17: The Thermodynamic Square

## Slide 18: The Four Fundamental Potentials
We now have four fundamental equations of state:
Memorizing these and their signs is tedious. Let’s use a mnemonic device…

## Slide 19: The Thermodynamic Square
Very Awesome Thermodynamics Under Graduate Students Help Professors!
Fig. 1: The thermodynamic square.

## Slide 20
Arrows point from S to T, and from P to V.

## Slide 21: How to Read the Square
Let’s find the differential for Helmholtz Free Energy ():
Natural Variables: The two corners adjacent to are and .
Coefficients: Look across the square.
  Across from is .
  Across from is .
Sign Rule: Move against arrow = negative. Move with arrow = positive.
  is against the arrow ()
  is against the arrow ()
Result: