## Slide 1: Flow work
Fluids flowing in pipes experience a pressure drop due to viscous and frictional losses.
To overcome these losses, a pump is used to supply work?
What is the flow work associated with fluid flow?
5 m
5 cm
Water 100kg/min
Tin= 300 K
Pin= 300 kPa
Water 100kg/min
Tout= 300 K
Pout= 290 kPa



## Slide 2: Flow work – fluid entering a pipe


FE = Pin*A
dx = dV/A


fluid element enters pipe
Fluid behind “pushes” the slug in
FE is +
Win > 0
Must do work on the fluid element for it to enter

## Slide 3: Flow work – fluid leaving a pipe


FE = Pout*A
dx = dV/A


fluid element leaves pipe
To exit the pipe, the fluid element has to push the downstream fluid out of the way
FE is -
Wout < 0
Fluid element does work to leave the pipe (loses energy)

## Slide 4: Flow work - example
Calculate the rate of flow work (energy/time = power)
5 m
5 cm
Water 100kg/min
Tin= 300 K
Pin= 300 kPa
Water 100kg/min
Tout= 300 K
Pout= 290 kPa


Wnet = Win + Wout = (PV)in – (PV)out

## Slide 5: Flow work - example
Calculate the rate of flow work (energy/time = power)
5 m
5 cm
Water 100kg/min
Tin= 300 K
Pin= 300 kPa
Water 100kg/min
Tout= 300 K
Pout= 290 kPa


Volumetric flow rate (m3/s)
30,000 J/min

## Slide 6: Flow work - example
Calculate the rate of flow work (energy/time = power)
5 m
5 cm
Water 100kg/min
Tin= 300 K
Pin= 300 kPa
Water 100kg/min
Tout= 300 K
Pout= 290 kPa


Volumetric flow rate (m3/s)
,000 J/min
The net work is > 0
This means you need to somehow supply work to make the fluid flow